## Slide 1
1
Networking module 5a
Network management: SDN and SNMP
Link layer part 1 - ARP
1

## Slide 2: Agenda
Repeat DNS
Routing (algorithms and protocols)
This module
SNMP
Software Defined Networking (SDN)
ARP

## Slide 3
3
Vorige week: DNS
Reminder: DNS
DNS security risks:
Use of DNS servers in DDOS attacks
DNS hijacking
Possible solutions:
DNS over HTTPS
DNSSec
Figure 1

## Slide 4
4
Vorige week: DNSSec
DNSSec signs DNS records, using public/private key cryptography
This provides authentication (but not confidentiality)
Similar to website certificates
Figure 19

## Slide 5
Vorige week: Routing
Reminder: routing & forwarding
Routing algorithms
  Link State – all nodes have complete view of network
  Distance Vector – node talks only to neighbours
Routing and Autonomous Systems
Routing Protocols
  Intra-AS Routing: OSPF (Link State)
  Inter-AS Routing: BGP (Distance Vector)
BGP hijacking
5
Figure 1

## Slide 6
6
Vorige week: Autonomous Systems
Autonomous Systems:
A group of routers under the same control
Belong to (for example) a single company or ISP
Intra-AS routing: routing within AS (i.e. OSPF)
Inter-AS routing: routing between AS’s (i.e. BGP)
Figure 9

## Slide 7
Intra-AS routing: OSPF (Open Shortest Path First)
OSPF - router advertisements flooded to entire AS
InteR-AS routing: BGP (border gateway protocol): the de facto inter-domain routing protocol --> “glue that holds the Internet together”

## Slide 8: Border Gateway Patrol Hijacking

## Slide 9
Path attributes and BGP routes
advertised network prefix includes BGP attributes:
  AS-PATH: list of AS-es through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
Policy-based routing:
  Policies determine whether a path is advertised and whether an advertised path will be accepted (e.g., never route through AS Y).
Route selection:
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria
9

## Slide 10: Will a BGP router always choose the route with the shortest AS_PATH length?
Yes, this is the actual purpose of the design
No, it chooses the path with the least next-hops
No, it uses policies. E.g. for political or economic reasons it might choose a different path
No, the BGP router always selects the loop-free route

## Slide 11
Network management
SNMP
Software Defined Networking
  SDN principles
  Match & Action
  SDN architecture
11
Figure 1

## Slide 12
SNMP: infrastructure for network management
managed device
managed device
managed device
managed device
definitions:
managed devices contain managed objects whose data is gathered into a Management Information Base (MIB)
managing
entity
data
managing entity
agent
data
agent
data
network
management
protocol
managed device
agent
data
agent
data
agent
data
12
Figure 9
Notes: 12

## Slide 13
SNMP protocol
Two ways to convey MIB info, commands:
agent
data
managed device
managing
entity
agent
data
managed device
managing
entity
trap msg
request
request/response mode
trap mode
response
13
Figure 10
Notes: 13

## Slide 14: SNMP Example

## Slide 15: Een 'managing server' wil weten hoe lang een bepaald 'managed device' (oftewel een agent) al online is. Hoe kan de managing server SNMP gebruiken om deze informatie te achterhalen?
Het MIB proces vraagt aan de agent hoe lang deze online is. De agent stuurt een reply met de waarde.
De informatie wordt uit de MIB gehaald op de managing server. Is deze informatie niet aanwezig dan stuurt de managing server een request naar de agent.
De MIB wordt via een gedistribueerd proces gesynchroniseerd tussen managing server en agent.
De gewenste informatie is opgeslagen in de MIB op het managed device. De server stuurt een SNMP request naar de agent om de info op te vragen. De agent stuurt een reply met de waarde van het opgevraagde object.

## Slide 16
Network Layer
The Network Layer can be divided into two parts:
Data plane – per router functions that determine how datagram is arriving and forwarded .
Control plane – Network wide logic that controls how datagram is routed (e.g. OSPF and BGP)
16
Figure 1

## Slide 17
traditionally dataplane and control plane have been implemented together in within router.
2005: renewed interest in rethinking network control plane  Software Defined Networking
2
3
0100 1101
values in arriving
packet’s header
logically-centralized routing controller
1
control plane
data plane
local flow table
headers counters actions
17
Figure 2

## Slide 18
Software defined networking (SDN)
Why a logically centralized control plane?
easier network management: avoid router misconfigurations, greater flexibility of traffic flows
table-based forwarding allows “programming” routers
  centralized “programming”: easier: compute tables centrally and distribute
  distributed “programming”: more difficult: compute tables as result of distributed algorithm (protocol) implemented in each and every router
open (non-proprietary) implementation of control plane
18

## Slide 19
Generalized Forwarding and SDN
2
3
0100 1101
values in arriving
packet’s header
logically-centralized routing controller
1
control plane
data plane
Each router contains a flow table that is computed and distributed by a logically centralized routing controller
local flow table
headers counters actions
19
Figure 2

## Slide 20
Openflow data plane abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller
* : wildcard
Flow table in a router (computed and distributed by controller) define router’s match+action rules
20
Figure 3

## Slide 21
Destination-based forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
51.6.0.8
*
*
*
port6
Examples
IP datagrams destined to IP 51.6.0.8 should be forwarded to router output port 6
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
*
*
*
*
22
drop
Firewall:
do not forward (block) all datagrams destined to TCP port 22
Destination-based layer 2 (switch) forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
*
*
*
port3
layer 2 frames from MAC 22:A7:23:11:E1:02 should be forwarded to output port 3
22:A7:23:
11:E1:02
21
Notes: 21

## Slide 22
Openflow abstraction
Router
  match: longest destination IP prefix
  action: forward out a link
Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port
match+action: unifies different kinds of devices
22

## Slide 23
SDN: data plane switches
Data plane switches
fast, simple, commodity switches implementing generalized data-plane forwarding in hardware
switch flow table computed, installed by controller
API for table-based switch control (e.g., OpenFlow)
  defines what is controllable and what is not
protocol for communicating with controller (e.g., OpenFlow)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
23
Figure 4

## Slide 24
SDN controller
SDN controller (network OS):
maintain network state information
interacts with network control applications “above” via northbound API
interacts with network switches “below” via southbound API
implemented as distributed system for performance, scalability, fault-tolerance, robustness
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
24
Figure 5

## Slide 25
SDN: control applications
network-control apps:
“brains” of control: implement control functions using lower-level services, API provided by SDN controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications
25
Figure 6

## Slide 26
Network-wide distributed, robust state management
Communication to/from controlled devices
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Interface, abstractions for network control apps
SDN
controller
routing
access
control
load
balance
Components of SDN controller
communication layer: communicate between SDN controller and controlled switches
Network-wide state management layer: state of networks links, switches, services: a distributed database
Interface layer to network control apps: abstractions API
26
Figure 7

## Slide 27
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra’s link-state
Routing
s1
s2
s3
s4
SDN: control/data plane interaction
S1, experiencing link failure using OpenFlow port status message to notify controller
1
SDN controller receives OpenFlow message, updates link status info
2
Dijkstra’s routing algorithm application has previously registered to be called when ever link status changes. It is called.
3
Dijkstra’s routing algorithm access network graph info, link state info in controller, computes new routes
4
27
Figure 8

## Slide 28
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra’s link-state
Routing
s1
s2
s3
s4
link state routing app interacts with flow-table-computation component in SDN controller, which computes new flow tables needed
5
Controller uses OpenFlow to install new tables in switches that need updating
6
SDN: control/data plane interaction
28
Figure 8

## Slide 29: Software Defined Networking
Een netwerk bestaat uit een aantal met elkaar verbonden routers. Eén van deze routers stelt vast dat een bepaalde verbinding offline is gegaan.
Vroeger zou deze router de andere routers hierover informeren met behulp van een routing protocol. Elke router zou vervolgens voor zichzelf de eigen routing table opnieuw berekenen,.
Leg uit, hoe SDN (Software Defined Networking) hier mee omgaat. Welke verschillende stappen worden gezet, om te zorgen dat de routing tables van alle routers geupdate worden.
Zet antwoord in chat

## Slide 30
The router will notify the central SDN controller about the link failure.
The SDN controller will invoke a network control application that will calculate new routing information.
Finally, the SDN controller will push the new routing tables to all routers (or packet switches).
Notice how the routers don't communicate directly with one another: the new routing information is calculated centrally and then distributed to the routers.

## Slide 31
Break
31

## Slide 32
Link layer
MAC addresses
Looking up MAC addresses: ARP
MAC addresses vs IP addresses, a routing example
32
Figure 1

## Slide 33
Link layer: reminder
terminology:
hosts and routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired links
  wireless links
  LANs
layer-2 packet: frame, encapsulates datagram
data-link layer has responsibility of
transferring datagram from one node
to physically adjacent node over a link
33
Figure 9
Notes: 33

## Slide 34
MAC addresses
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
MAC (or LAN or physical or Ethernet) address:
  function: used ‘locally” to get frame from one interface to another physically-connected interface (same network, in IP-addressing sense)
  48 bit MAC address burned in NIC ROM
  e.g.: 1A-2F-BB-76-09-AD
34
hexadecimal (base 16) notation
(each “number” represents 4 bits)
Notes: 34

## Slide 35
MAC addresses (more)
each adapter on LAN has unique MAC address
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC flat address ➜ portability
  can move LAN card from one LAN to another
IP hierarchical address not portable
  address depends on IP subnet to which node is attached
35
That’s why you can recognise your Raspberry Pi by its MAC address
Notes: 35

## Slide 36
ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
36
Question: how to determine
interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88
Figure 10
Notes: 36

## Slide 37
ARP protocol: same LAN
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator
37
Notes: 37

## Slide 38: Leg uit welke functie het TTL veld heeft in een ARP tabel.
Door een Time To Live in te stellen wordt voorkomen dat de ARP tabel te groot wordt.
Time To Live zorgt er voor dat de verstuurde data onbruikbaar wordt voor de ontvanger na een bepaalde periode. Hiermee wordt de ontvanger gedwongen opnieuw een request te doen.
Als de Time To Live van een entry verloopt, dan wordt de entry verwijderd uit de ARP tabel. Door verouderde entries te verwijderen, wordt de informatie in de tabel up to date gehouden.
De Time To Live zorgt er voor dat een tabel maar een bepaalde tijd te bezoeken is. Hierdoor wordt een DDOS aanval op ARP voorkomen.

## Slide 39
Addressing: routing to another LAN
walkthrough: send datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame)
  assume A knows B’s IP address
  assume A knows IP address of first hop router, R (how?)
  assume A knows R’s MAC address (how?)
39
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
Figure 11
Notes: 39

## Slide 40
40
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame with R's MAC address as dest, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
Addressing: routing to another LAN
Figure 12
Notes: 40

## Slide 41
41
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222
Addressing: routing to another LAN
Figure 13
Notes: 41

## Slide 42
42
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy
Addressing: routing to another LAN
Figure 14
Notes: 42

## Slide 43
43
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy
Addressing: routing to another LAN
Figure 15
Notes: 43

## Slide 44
44
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
Addressing: routing to another LAN
Figure 16
Notes: 44

## Slide 45
Network management
Software Defined Networking
  SDN principles
  Match & Action
  SDN architecture
45
Figure 1

## Slide 46
Ethernet
Ethernet
“dominant” wired LAN technology
simple, cheap
kept up with speed race: 10 Mbps – 10 Gbps
Ethernet frame
Preamble: fixed pattern used to synchronise sender, receiver clocks
Source and Destination MAC address
Type: usually IP
Data: contains IP datagram
CRC: cyclic redundancy check code to detect errors (corrupt frames are dropped)
Figure 18
dest.
address
source
address
data (payload)
CRC
preamble
type
Figure 17
Notes: 46

## Slide 47
Ethernet and switches
Collision domains
One host can send at the same time, hosts need to wait when line is busy
When two hosts start sending at the same time, data collides and becomes corrupted.
All of this decreases performance
Bus topology: popular through mid 90s
  all nodes in same collision domain
Star topology: prevails today
  active switch in center
  each “spoke” runs a (separate) Ethernet (nodes do not collide with each other)
bus
switch
star
Figure 19
Notes: 47

## Slide 48
Switch: multiple simultaneous transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
48
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
Figure 20
Notes: 48

## Slide 49
Switch forwarding table
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
49
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
Figure 21
Notes: 49

## Slide 50
frame destination, A’, location unknown:
50
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table - initially empty
A
1
60
A A’
A A’
A A’
A A’
A A’
flood
A’ A
destination A location known:
A’
4
60
selectively send on just one link
Switch: self-learning
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender
  records sender/location pair in switch table
  switches do NOT use ARP
Figure 22
Notes: 50

## Slide 51
Switches vs. Routers
both are store-and-forward:
routers: network-layer devices - examine network-layer headers - connect different subnets
switches: link-layer devices - examine link-layer headers - connect devices on same subnet
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using MAC addresses
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram
51
Figure 23
Notes: 51

## Slide 52
52
Next module lecture: Wireless networks
Homework - before the next lecture:
  study the materials as described in the study guide on DLO
  make practice test #4
  finish this modules labs and hand in your results on DLO
For next module…

## Slide 53
53
Next modules lecture: Link layer (pt. 2) & Wireless networks
To prepare for next mosules practical lab: read chapter 5.7 on SNMP in Kurose & Ross!!!
For next module…

## Slide 54
Sources
Figure 1-23: Kurose and K.W. Ross, Computer Networking, A Top-Down Approach, Pearson Education, 2016
54

## Slide 55
Sources
Figure 1,2,3,4,5,6,8,10,11,12,13,14,15,16: Kurose and K.W. Ross, Computer Networking, A Top-Down Approach, Pearson Education, 2016
55